## Slide 1: STM32MP1 Workshop Linux Host Setup to go further with the Packages if using Linux native, virtual box

## Slide 2: Additional Setup
Additional Linux Host Setup
After the workshop to go further ,If using Linux native, virtual box,
to be able to compile the Linux Kernel, TF-A, Uboot, Optee with the developer package, or to burn a SDcard with STM32CubeProgrammer,
additional installations after Linux-host pre-requisite are needed.
Please follow next slides
The pre-configured VM image for VMWare Player contains already theses installations
OPTIONAL

## Slide 3: Additional Setup Summary
Additional Setup summary
A-Starter Package Install
B-Developer Package Install
B.1-Install Linux Kernel
B.2-Install TF-A
B.3-Install U-Boot
C-Tool Install
C.1-Install CubeProgrammer
1 to 2 hour work
OPTIONAL

## Slide 4
Additional Setup
Packages Installation tree
  At the end of the Starter and Developer Packages installation
  Note : In terminal console, Developer Package root will be defined in $SDK_ROOT to /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package/
SDK (see for install LinuxHost_Setup_ForStm32MP1.pptx) Kernel,TF-A,Uboot Source code

## Slide 5: A-Starter Package Install
OPTIONAL

## Slide 6: Getting started: Starter Package
Install Starter Package
  Download en.FLASH-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz from
  https://wiki.st.com/stm32mpu/wiki/STM32MP1_Starter_Package_-_images
  to directory structure
  https://wiki.st.com/stm32mpu/wiki/Example_of_directory_structure_for_Packages
  /local/STM32MP15-Ecosystem-v1.0.0/Starter-Package
  cd /local/STM32MP15-Ecosystem-v1.0.0/Starter-Package
  tar xvf en.FLASH-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz
OPTIONAL

## Slide 7: B-Developer Package Install
OPTIONAL

## Slide 8: B.1-Developer Package Install Linux Kernel
OPTIONAL

## Slide 9: Getting started: Developer Package Linux Kernel
Install Developer Package Linux Kernel
  1. Edit $HOME/.bashrc and add
  export SDK_ROOT=/local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  2. Download en.SOURCES-kernel-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz
  from
  https://wiki.st.com/stm32mpu/index.php/STM32MP1_Developer_Package
  to directory structure
  (cf https://wiki.st.com/stm32mpu/wiki/Example_of_directory_structure_for_Packages)
  /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  cd /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  tar xvf en.SOURCES-kernel-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz
OPTIONAL

## Slide 10: Getting started: Developer Package Linux Kernel
Install Developer Package Install Linux kernel
cd $SDK_ROOT/stm32mp1-openstlinux-4.19-thud-mp1-19-02-20/sources/arm-openstlinux_weston-linux-gnueabi/linux-stm32mp-4.19-r0
tar xvf linux-4.19.9.tar.xz
source $SDK_ROOT/SDK/environment-setup-cortexa7t2hf-neon-vfpv4-openstlinux_weston-linux-gnueabi
cd linux-4.19.9
for p in `ls -1 ../*.patch`; do patch -p1 < $p; done
make multi_v7_defconfig fragment*.config
for f in `ls -1 ../fragment*.config`; do scripts/kconfig/merge_config.sh -m -r .config $f; done
yes '' | make oldconfig
OPTIONAL

## Slide 11: Getting started: Developer Package Linux Kernel
Install Developer Package Build Linux kernel
make uImage vmlinux dtbs LOADADDR=0xC2000040
make modules
mkdir –p $PWD/install_artifact/
make INSTALL_MOD_PATH="$PWD/install_artifact" modules_instal
OPTIONAL

## Slide 12: B.2-Developer Package Install TF-A
OPTIONAL

## Slide 13: Getting started: Developer Package TF-A
Install Developer Package TF-A
  Download en.SOURCES-tf-a-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz from
  https://wiki.st.com/stm32mpu/index.php/STM32MP1_Developer_Package
  to directory structure
  https://wiki.st.com/stm32mpu/wiki/Example_of_directory_structure_for_Packages
  /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  cd /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  tar xvf en.SOURCES-tf-a-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz
OPTIONAL

## Slide 14: Getting started: Developer Package TF-A
Install Developer Package Install TF-A
cd $stm32mp1-openstlinux-4.19-thud-mp1-19-02-20/sources/arm-openstlinux_weston-linux-gnueabi/tf-a-stm32mp-2.0-r0/
tar xvf v2.0.tar.gz
cd arm-trusted-firmware-2.0
for p in `ls -1 ../*.patch`; do patch -p1 < $p; done
OPTIONAL

## Slide 15: Getting started: Developer Package TF-A
Install Developer Package Build TF-A
source $SDK_ROOT/SDK/environment-setup-cortexa7t2hf-neon-vfpv4-openstlinux_weston-linux-gnueabi
make -f $PWD/../Makefile.sdk all
OPTIONAL

## Slide 16: B.3-Developer Package Install U-Boot
OPTIONAL

## Slide 17: Getting started: Developer Package U-Boot
Install Developer Package U-Boot
  Download en.SOURCES-u-boot-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz from
  https://wiki.st.com/stm32mpu/index.php/STM32MP1_Developer_Package
  to directory structure
  https://wiki.st.com/stm32mpu/wiki/Example_of_directory_structure_for_Packages
  /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  cd /local/STM32MP15-Ecosystem-v1.0.0/Developer-Package
  tar xvf en.SOURCES-u-boot-stm32mp1-openstlinux-4.19-thud-mp1-19-02-20.tar.xz
OPTIONAL

## Slide 18: Getting started: Developer Package U-Boot
Install Developer Package Build U-Boot
cd $stm32mp1-openstlinux-4.19-thud-mp1-19-02-20/sources/arm-openstlinux_weston-linux-gnueabi/u-boot-stm32mp-2018.11-r0/
tar xvf v2018.11.tar.gz
cd u-boot-2018.11
for p in `ls -1 ../*.patch`; do patch -p1 < $p; done
OPTIONAL

## Slide 19: Getting started: Developer Package U-Boot
Install Developer Package Build U-Boot
source $SDK_ROOT/SDK/environment-setup-cortexa7t2hf-neon-vfpv4-openstlinux_weston-linux-gnueabi
make -f $PWD/../Makefile.sdk all
OPTIONAL

## Slide 20: C-Tool Install
OPTIONAL

## Slide 21: C.1-Tool Install Cube Programmer
OPTIONAL

## Slide 22: Getting started: Tools Cube Programmer
Install Tools : CubeProgrammer
https://wiki.st.com/stm32mpu/index.php/STM32CubeProgrammer
Get SetupSTM32CubeProgrammer v2.0.0.zip and move it to Linux Host in $HOME/Desktop
cd $HOME/Desktop
unzip "SetupSTM32CubeProgrammer v2.0.0.zip" -d "./SetupSTM32CubeProgrammer v2.0.0"
cd ~/Desktop/SetupSTM32CubeProgrammer\ v2.0.0/
./SetupSTM32CubeProgrammer-xxx.linux
sudo ln –s $HOME/STMicroelectronics/STM32Cube/STM32CubeProgrammer/bin/STM32_Programmer_CLI $HOME/bin/STM32_Programmer_CLI
OPTIONAL

## Slide 23: Getting started: Tools Cube Programmer
Install Tools : CubeProgrammer
Install DFU USB driver for USB OTG
sudo apt-get install libusb-1.0-0
sudo cp $HOME/STMicroelectronics/STM32Cube/STM32CubeProgrammer/Drivers/rules/*.* /etc/udev/rules.d/
Install java
sudo apt-get install openjfx
Launch
$HOME/STMicroelectronics/STM32Cube/STM32CubeProgrammer/bin/STM32CubeProgrammer
OPTIONAL

## Slide 24: Thanks