## Slide 1: STM32MP1
Coprocessing and scalability from MCU to MPU

## Slide 2: Coprocessing Management overview

## Slide 3: Coprocessing Software Framework
Dual Cortex-A7 @ 650MHz
MCU + Ret. RAM
448kB
Mailbox
IPCC
Cortex-M4 @ 200MHz
Framework from Community
RPMsg
RemoteProc
VirtIO
Library from ST
OpenAMP
application
application

## Slide 4: Coprocessing Linux Framework
A list of services are proposed relying on the open-source RemoteProc/RPMsg frameworks and IPCC hardware peripheral:
  Load and control Cortex®-M4 firmware by Cortex®-A7
  Inter-processor communication based on messages and mailboxes
  Resources management
    Peripheral assignment to a Core (with access right check)
    System resources management (resources that are common to both cores)

## Slide 5: Firmware loading
The Cortex-M4 firmware is loaded by Cortex-A thanks to services provided by OpenSTLinux RemoteProc framework, uses a resource table to define commun resources (ring buffers and trace buffers).
Firmware is stored in an ELF format file, in OpenSTLinux filesystem /lib/firmware
Load of the firmware is done either :
  Automatically when OpenSTLinux has started
  Manually at runtime thanks to RemoteProc interface
OpenSTLinux load an control the Cortex-M4 firmware execution

## Slide 6: Firmware loading
ST
Community
3rd Party
Hardware
Legend
application
stm32_rproc
MCUSRAM/RETRAM
rproc_core
/sys/class/remoteproc/remoteprocX/
STM32Cube firmware
Step 1: Cortex-M4 Firmware is loaded from the file system. It can be loaded during kernel probe or at runtime by an application using sysfs.
Cortex-A
OpenST
Linux
Cortex-M
RCC
Step 2: Cortex M4 is clocked and reset is de-asserted to start M4 firmware
Resource table

## Slide 7: Inter-Processor Communication
Dual Cortex-A7 @ 650MHz
MCU + Ret. RAM
448kB
Mailbox
IPCC
Cortex-M4 @ 200MHz
Framework from Community
RPMsg
RemoteProc
VirtIO
Library from ST
OpenAMP
Mailbox management is seen as standard protocol (UART, I2C ..)
application
application
virtual_hal_uart
Library from ST
stm32_rpmsg_tty
/dev/ttyRPMSG

## Slide 8: Shared RAM memory mapping
Retention RAM (64kB)
MCUSRAM1 (128kB)
MCUSRAM2 (128kB)
MCUSRAM3 (64kB)
MCUSRAM4 (64kB)
Rev A: SRAM3 (128kB)
Rev B: SRAM3 (64kB) + SRAM4 (64kB)
Cortex-A7 Non-Secure
Cortex-A7 Non-Secure
Cortex-M4
Cortex-M4
Exception table
Code & Data
Code
Data
DMA buffers
Inter Process Communication (IPC) buffers
Cortex-M firmware must start at address 0 of the RETRAM, but can be partially located in MCUSRAM
Each customer can of course tune this mapping (regions location and sizes) to fit with his product needs

## Slide 9
Resources management
OpenSTLinux since beta release for system on A7.M4 seen as a coprocessor.
  Masters the resource allocation split between cores (Hw context execution for each IP
  For the peripheral allocated to Cortex-M4 ensures reservation of their Clock and GPIOs.
  Controls M4 resources (for GPIO, clock config runtime modifications, the M4 asks to A7).
Linux system master the resource allocation to M4

## Slide 10: Shared resource configuration set
Whereas some of these resources are instantiated for each core, some other ones, defined as shared resources, are shared by both cores. To avoid contention on these shared resources, they must be controlled by only one core: the Cortex-A which is natively running Linux. The shared resources are:
  Clock tree: the clock configuration is managed by the Linux clock framework, the coprocessor is in charge of the clock gating for the peripheral. Not the configuration (frequency)
  Pin: the pin configuration is managed by the Linux pinctrl framework. The coprocessor initializes and controls its GPIO and has to declare them to resource manager
  Regulator: the power supply is managed by Linux regulator framework.
  External interrupt (EXTI): EXTI interrupt is managed by Linux regulartor framework. The coprocessor configures EXTI line and enable the NVIC interrupt. It has to declare its assigned EXTI line(s) to resource manager
The resource configuration service is mainly managed on Cortex-A by Linux. A remote processor shared resource manager (rproc_srm) reserves the shared resources of a peripheral assigned to Cortex-M coprocessor.
Shared resource configurations are based on DeviceTree declaration of shared resource associated to a peripheral

## Slide 11: Shared resource configuration set
Peripheral XXX
remoteproc
rproc_srm_core
rproc_srm_dev
rproc_srm_dev
rproc_srm_dev
Cortex-A
OpenST
Linux
Cortex-M
application
PWR
RCC
GPIO
EXTI
User space
Kernel space
Hardware
HAL_Cortex
HAL_XXX
HAL_GPIO
HAL_RCC
Configure & Drive output GPIOs
Reserves EXTI interrupts, GPIOs, clock and regulators for Cortex-M XXX peripheral
Configure EXTI
Mask / unmask
EXTI interrupts
Enable / disable the peripheral clocks. Cannot change the system clock tree
application
HAL_..._MSP
ST
Community
3rd Party
Hardware
Legend

## Slide 12: Software Implementation
    @ soc {
    i2c1: i2c@40012000 {
    compatible = "st,stm32f7-i2c";
    status = “disabled";
    }
    };
    @M4_hw_resources {
    compatible = "rproc-srm-core";
    status = “enable";
M4_IP_I2C@0x400012000 {
compatible = “rproc-srm-dev";
status = “okay";
clocks = <&rcc_clk I2C1_K>;
pinctrl-0 = <i2c1_pins_a>;
    };
    };
I2C peripheral drive is disabled on Cortex-A7
I2C peripheral is declared as Cortex-M4 resource and enabled. GPIO and clock used by I2C peripheral are declared.
void HAL_I2C_MspInit(I2C_HandleTypeDef *hi2c)
{
…
#if CONFIG_MASTER_MODE
/*##-1- Enable the HSI clock #*/
RCC_OscInitStruct.OscillatorType = RCC_OSCILLATORTYPE_HSI;
RCC_OscInitStruct.HSIState = RCC_HSI_ON;
RCC_OscInitStruct.HSICalibrationValue = RCC_HSICALIBRATION_DEFAULT;
if (HAL_RCC_OscConfig(&RCC_OscInitStruct)!= HAL_OK)
{
/* Error */
while(1);
}
/*##-2- Configure HSI as I2C clock source #*/
RCC_PeriphCLKInitStruct.PeriphClockSelection = RCC_PERIPHCLK_I2Cx;
RCC_PeriphCLKInitStruct.I2c123ClockSelection = RCC_I2CxCLKSOURCE;
HAL_RCCEx_PeriphCLKConfig(&RCC_PeriphCLKInitStruct);
#endif
/*##-3- Enable peripherals and GPIO Clocks #################################*/
/* Enable GPIO TX/RX clock */
I2Cx_SCL_GPIO_CLK_ENABLE();
I2Cx_SDA_GPIO_CLK_ENABLE();
/* Enable I2Cx clock */
I2Cx_CLK_ENABLE();
/*##-4- Configure peripheral GPIO ##########################################*/
HAL_GPIO_Init(I2Cx_SCL_GPIO_PORT, &GPIO_InitStruct);
HAL_GPIO_Init(I2Cx_SDA_GPIO_PORT, &GPIO_InitStruct);
}
Clock gating is handled by Cortex-M4
System clock tree HSI clocking is handled by Cortex-A7
GPIO configuration is handled by Cortex-M4
Cortex-A
OpenST
Linux
Cortex-M
A7 : Linux Device Tree
M4 : HAL Init
Code generated by STM32CubeMX !

## Slide 13: STM32CubeMX Coproc Management
STM32CubeMX ease co-processing System Resource management by generating
  OpenSTLinux device tree configuration for resource allocation
  Cortex-M4 coprocessor code (as for legacy STM32)

## Slide 14: Coproc Management Reset Case
There can be have separate reset for Cortex-A7 et Cortex-M4
Example:
  Crash on linux side can reset Cortex-A7 without impacting Cortex-M4

## Slide 15: STM32MP1 Coprocessing
Architecture for real time applications
Easy configuration and use of Cortex-M4 inside STM32MP1
STM32 Knowledge and Ecosystem
Notes:   Real time control and monitoring
  Deterministic sensor control
  Low power applications (i.e. vs. Cortex-A)

## Slide 16
Thank you!