## Slide 1: STM32MP1 How to update the Software Release

## Slide 2: Example : How to update kernel component

## Slide 3: Update kernel release
Update kernel release with github
The software packages are delivered only for Major Releases.
Minor Releases are available in
https://wiki.st.com/stm32mpu/wiki/STM32MP15_OpenSTLinux_release_note
Section 8 Minor release updates
Minor Release allows to provide ST fixes on major release.
Example with kernel :
Kernel sources are delivered under github containing all fixes found by ST : in github release v4.19-stm32mp-r1.2
How to get kernel github release using git clone command
git clone https://github.com/STMicroelectronics/linux.git tags/v4.19-stm32mp-r1.2
The same mechanism exists for all components of developer package (U-Boot, TF-A, OPTee)
Notes:   Let's start your OpenSTLinux on discovery !

## Slide 4: Update kernel release in developer package
Update kernel release with github
It is possible to :
Extract a patch you need and apply it to your current developer package
(using git format-patch to extract the patch from github)
Or
Directlty use the latest kernel version under github (with all ST patches)
(build with github is also described in File:Linux.README.HOW TO.txt)
WARNING: Way of working is to stay as much as possible close to LTS release delivered in developer package, so better to take only needed fixes.
ST fixes are up streamed to community but may make take long time.
ST delivers new software packages (Major Release every 6 months)
Notes:   Let's start your OpenSTLinux on discovery !

## Slide 5: Example : kernel patch in developer package
Display fix example
https://community.st.com/s/question/0D50X0000ASoi2XSQR/stm32mp157cdk2-not-booting-to-weston-gtk-demo-launcher
0066-drm-panel-otm8009a-add-delay-before-switch-to-video-.patch
0065-drm-panel-otm8009a-fix-clock-to-29.70-Mhz.patch
Copy patches from stm32mp1-openstlinux-19-02-20-github-display-fix.zip to directory
$SDK_ROOT/stm32mp1-openstlinux-4.19-thud-mp1-19-02-20/sources/arm-openstlinux_weston-linux-gnueabi/linux-stm32mp-4.19-r0
Rebuild the kernel
Copy new uImage from arch/arm/boot/uImage to /boot/uImage of the target
Flash Image also available in FLASH-stm32mp1-openstlinux-19-02-20-github-display-fix.tar.xz
https://community.st.com/s/contentdocument/0690X00000889m3QAA
Notes:   Let's start your OpenSTLinux on discovery !

## Slide 6: Update release in distribution package
Update release with github
How to switch to github® mode in distribution package.
https://wiki.st.com/stm32mpu/wiki/OpenSTLinux_distribution#Reference_source_code
Notes:   Let's start your OpenSTLinux on discovery !

## Slide 7: Thanks